## Slide 1
Icarus Verilog Installation Guide
for Mac OS Users

## Slide 2: Contents
Icarus Verilog Installation
GTKwave Installation
Example Code

## Slide 3: Icarus Verilog
An implementation of the Verilog hardware description language
Most commonly used in the design and verification of digital circuits at the register-transfer level of abstraction
A hardware description language (HDL) used to model electronic systems

## Slide 4: Homebrew
Package Management Application for macOS
Mostly Used for installing Command-Line Tools or System Packages

## Slide 5: Homebrew Installation - brew.sh

## Slide 6: Homebrew Installation
Click Here!
Copy this script (cmd + c / Click the button on the right)

## Slide 7: Homebrew Installation
Open your Terminal application

## Slide 8: Homebrew Installation
Paste the copied script

## Slide 9: Homebrew Installation
Input your password

## Slide 10: Homebrew Installation
Follow the instruction (Press RETURN/ENTER)

## Slide 11: Homebrew Installation
Installation Finished!

## Slide 12: Icarus Verilog Installation
At brew.sh, you can search for the package that you want to install

## Slide 13: Icarus Verilog Installation

## Slide 14: Icarus Verilog Installation
Paste the copied script

## Slide 15: Icarus Verilog Installation
Check your installation by typing ‘iverilog’ at the terminal
Finished!

## Slide 16: GTKWave
Wave Analyzer for standard Verilog VCD/EVCD files

## Slide 17: GTKWave Installation
Download file at https://sourceforge.net/projects/gtkwave/files/
or, input command “brew install gtkwave” at terminal

## Slide 18: GTKWave Installation
Click the gtkwave.app with RMB and open (to avoid apple’s security warning)

## Slide 19: Make Testfiles
By using text editor (like vi, notepad, VSCode etc.)
Make sure filename extension is ‘v’

## Slide 20: Make Testfiles
test.v
testbench.v

## Slide 21: Make Testfiles
Input command “iverilog -o test test.v testbench.v”
Input command “vvp test”

## Slide 22: Make Testfiles
Open test.vcd on gtkwave